## Slide 1: RadioInstigator
Signals Intelligence Platform

## Slide 2: Who am I?
Josh Conway (CrankyLinuxUser)
FCC Amateur radio: KC9JEF Facial Recog for your ‘Con (CPU bound, no gpu, no internet) https://hackaday.com/2015/03/04/face-recognition-for-your-next-con/ Multisite Home/Office/Hackerspace Automation
https://hackaday.io/project/12985-multisite-homeofficehackerspace-automation
Thalmic Labs(North) Shuts Down Free Developer Access Update: It’s Back Again https://hackaday.com/2014/11/18/thalmic-labs-shuts-down-free-developer-access/

## Slide 3: What is this “Radio” thing, anyways?

## Slide 4: Is this a radio? Is that a radio???

## Slide 5: They all are!
Definition (noun): The transmission and reception of electromagnetic waves of radio frequency, especially those carrying sound messages.
Definition (verb): communicate or send a message by radio.

## Slide 6: Signals Intelligence
Signals intelligence (SIGINT) is intelligence-gathering by interception of signals, whether communications between people (communications intelligence—abbreviated to COMINT) or from electronic signals not directly used in communication (electronic intelligence—abbreviated to ELINT).
-- Wikipedia
BUT WHY DO WE CARE???

## Slide 7: Common household things… Right?

## Slide 8: Security? Not if we can get away without it!
How many of these are implemented on radios you own?
Are they secure?
Are you sure???

## Slide 9: …. Don’t mind if I do!
Unknown
hardware
Unencrypted

## Slide 10
We are watching you

## Slide 11: My Platform - A $150 Signals Intelligence Tablet
Raspberry Pi 3 B+
HDMI Touchscreen
RTL-SDR
Keyboard
Cool prints!

## Slide 12: You want to build one?

## Slide 13: SigInt on a shoestring or Dirty SigInt Deeds Done Dirt Cheap

## Slide 14: The Notorious RTL-SDR
GOOD | BAD
Cheap Easy to obtain 24MHz-1766MHz 2.4MHz Bandwidth (window) | Cheap Sometimes dubious build quality Janky included antennas

## Slide 15: ADALM-PLUTO
GOOD | BAD
$100-$150 Uber-hackable (dual core Arm with Linux) 70MHz-6GHz (?!) 20MHz Bandwidth (window) Can run programs on device! | Can be hard to obtain 5mW Tx Janky included antennas USB2 limits overall bandwidth

## Slide 16: HackRF
GOOD | BAD
~$300 Very well supported 1MHz-6GHz (?!?!) Sweep Mode – 8GHz/second | Simplex (Can Tx or Rx, not at the same time) 8 bit IQ

## Slide 17: KerberosSDR
GOOD | BAD
~$125 Coherent Quad RTL-SDR 24MHz-1.7GHz | Toolchain very ‘raw’ because new 8 bit IQ

## Slide 18: Antennas … Because the ones with the SDR suck

## Slide 19: Omnidirectional Antennas
Horizontal
Polarization
Vertical
Polarization

## Slide 20: Yagi Antennas

## Slide 21: Yagi Antennas cont’d

## Slide 22: Log Parabolic Antennas

## Slide 23: Log Parabolic Antennas

## Slide 24: Vivaldi Antennas

## Slide 25: Software Whisperer (OS, Libraries)
RPITX Library RTL_SDR Libraries

## Slide 26: Software / GQRX

## Slide 27: Salamandra - Spy Microphone Detector

## Slide 28: TempestSDR - Every Monitor is Wireless

## Slide 29: Demotime….

## Slide 30: You want to build one?

## Slide 31: RadioInstigator
Signals Intelligence Platform
Josh Conway